SPECIFICATIONS FOR 0-5V/0-2A DUAL OUTPUT DC POWER SUPPLY

| 1. | Model no |  | : UE-DPS-25. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-5V Dual output continuously variable with coarse & |
|  |  |  |  | Fine potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-2A Dual output continuously variable with coarse & |
|  |  |  |  | fine potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 1mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

| 9. | Indication(s) | : a) One LED for input, |
| --- | --- | --- |
|  |  | b) One LED each for CV and CC indication, |
|  |  | c) One 3½ digit digital panel meter is provided |
|  |  | to read output voltage, |
|  |  | d) One 3½ digit digital panel meter is provided |
|  |  | to read output current. |
| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 5V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 2A, |
|  | NOTE | :d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-15V/0-1A DUAL OUTPUT DC POWER SUPPLY

| 1. | Model no |  | : UE-DPS-25. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-15V Dual output continuously variable with coarse & |
|  |  |  |  | Fine potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-1A Dual output continuously variable with coarse & |
|  |  |  |  | fine potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

| 9. | Indication(s) | : a) One LED for input, |
| --- | --- | --- |
|  |  | b) One LED each for CV and CC indication, |
|  |  | c) One 3½ digit digital panel meter is provided |
|  |  | to read output voltage, |
|  |  | d) One 3½ digit digital panel meter is provided |
|  |  | to read output current. |
| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 15V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 1A, |
|  | NOTE | :d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-32V/0-2A DUAL OUTPUT DC POWER SUPPLY

| 1. | Model no |  | : UE-DPS-56. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-32V Dual output continuously variable with coarse & |
|  |  |  |  | Fine potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-2A Dual output continuously variable with coarse & |
|  |  |  |  | fine potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 3mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 32V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 2A, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |