SPECIFICATIONS FOR 12V/3A FIXED OUTPUT DC POWER SUPPLY

| 1. | Model no |  | : UE-FPS-42. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 12V DC, ± 3V adjustable by potentiometer |
|  |  |  |  |  | mounted on front panel with lock nut. |
|  |  |  | b) Current | : | 3A adjustable by potentiometer |
|  |  |  |  |  | mounted on front panel with lock nut. |
| 5. |  | Line Regulation | : Better than 0.1% for a line change voltage of |
|  |  |  |  |  | 230V AC ± 10%. |
| 6. |  | Load Regulation | : Better than 0.1% from no load to full load |
|  |  |  |  |  | and vice versa. |
| 7. | Ripple |  | : Less than 5mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for Output,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  |  | b) One Coarse potentiometer to |
|  |  |  | Control the output voltage & Current. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  |  | you. |
| 12. | Cooling | : Natural air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  |  | Strip with remote sensing at rear panel if |
|  |  |  | Required. |

SPECIFICATIONS FOR 24V/10A FIXED OUTPUT DC POWER SUPPLY

| 1. | Model no |  | : UE-FPS-EC-01A. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 250, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 24V DC, ± 3V adjustable by potentiometer |
|  |  |  |  |  | mounted on front panel with lock nut. |
|  |  |  | b) Current | : | 10A adjustable by potentiometer |
|  |  |  |  |  | mounted on front panel with lock nut. |
| 5. |  | Line Regulation | : Better than 0.5% for a line change voltage of |
|  |  |  |  |  | 230V AC ± 10%. |
| 6. |  | Load Regulation | : Better than 0.5% from no load to full load |
|  |  |  |  |  | and vice versa. |
| 7. | Ripple |  | : Less than 10mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  |  | Continuous short circuits |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC indication,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  |  | b) One Coarse potentiometer to |
|  |  |  | Control the output voltage & current. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  |  | Strip with remote sensing at rear panel if |
|  |  |  | Required. |

SPECIFICATIONS FOR 24V/20A FIXED OUTPUT DC POWER SUPPLY

| 1. | Model no |  | : UE-FPS-04. |  |
| --- | --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |  |
| 4. | Output | a) Voltage | : | 24V DC, ± 1V adjustable by potentiometer |
|  |  |  |  |  | mounted on front panel with lock nut. |
|  |  |  | b) Current | : | 20A Max adjustable by potentiometer |
|  |  |  |  |  | mounted on front panel with lock nut. |
| 5. |  | Line Regulation | : Better than 0.1% for a line change of 207V to |
|  |  |  |  |  | 253V. |  |
| 6. |  | Load Regulation | : Better than 0.1% from | no load to full load and |
|  |  |  |  |  | vice versa. |  |
| 7. | Ripple |  | : Less than 3mV (RMS) | or 100mV peak to peak. |
| 8. |  | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC indication,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : | a) One ON/OFF switch to ON/OFF the Unit. |
| --- | --- | --- | --- |
|  |  |  |  | b) One Coarse potentiometer to |
|  |  |  |  | Control the output voltage & current. |
| 11. | Mechanical | : | Bench top / 19” Rack Mounting as required by |
|  |  |  |  | you. |
| 12. | Cooling | : | Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : | Separate piri Terminal Block on Front Panel for |

Input(AC) and Output(DC) and for Remote sensing