SPECIFICATIONS FOR 0-32V/0-2A, +/- 0-15V/0.5A, 0-5V/3A MULTI

OUTPUT POWER SUPPLY

| 1. | Model no | : UE-MPS-64D. |
| --- | --- | --- |
| 2. | Mains input | : 230V, +10%, 50-60Hz, Single phase. |
| 3. | Type | : CV/CC. |
| 4. | Output | : a) 0-32V/0-2A , b) +/-15V/0.5A , c) 0-5V/3A. |
| 5. | Line Regulation | : + 0.1% max. Output Voltage for + 10% change |
|  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  | to full load or Vice-versa. |
| 7. | Ripple | : Less than 1mV R.M.S. |
| 8. | Protections | : a) Unit is protected by input fuse. |
|  |  | b) Unit is protected against input surges. |
|  |  | c) Output is protected against over loads & |
|  |  | Continuous short circuits |

9. Indication(s)	:    a) One LED for input

- One LED each for CV and CC indication

- One 3½ digit digital panel meter is provided to read output voltage.

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit. |
| --- | --- | --- |
|  |  | b) one coarse and one fine potentiometer to |
|  |  | Control the output voltage. |
|  |  | c) One Coarse and one fine potentiometer to |
|  |  | Control the output current. |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 5V/6A,24V/3A,15V/6A,-15V/6A,-5V/6A

MULTI OUTPUT POWER SUPPLY

| 1. | Model no | : UE-MPS-101. |
| --- | --- | --- |
| 2. | Mains input | : 230V, +10%, 50-6Hz, Single phase. |
| 3. | Type | : CV/CC. |
| 4. | Output | : a) 5V/6A, b) 24V/3A, c) 15V/6A, d) -15V/6A |
|  |  | e)-5V/6A. |
| 5. | Line Regulation | : + 0.1% max. Output Voltage for + 10% change |
|  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  | to full load or Vice-versa. |
| 7. | Ripple | : Less than 1mV R.M.S. |
| 8. | Protections | : a) Unit is protected by input fuse, |
|  |  | b) Unit is protected against input surges, |
|  |  | c) Output is protected against over loads & |
|  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC indication ,

,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  | b) One Coarse and one fine potentiometer to |
|  |  | Control the output voltage, |
|  |  | c) One Coarse and one fine potentiometer to |
|  |  | Control the output current, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 6V,8V,12V,24V/8 4A MULTI OUTPUT POWER

SUPPLY

| 1. | Model no | : UE-MPS-96. |
| --- | --- | --- |
| 2. | Mains input | : 220V, +10%, 50-6Hz, Single phase. |
| 3. | Type | : CV/CC. |
| 4. | Output | : 6V, 8V,12V,24V/8 4A |
| . |  |  |
| 5. | Line Regulation | : + 0.1% max. Output Voltage for + 10% change |
|  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  | to full load or Vice-versa. |
| 7. | Ripple | : Less than 1mV R.M.S. |
| 8. | Protections | : a) Unit is protected by input fuse, |
|  |  | b) Unit is protected against input surges, |
|  |  | c) Output is protected against over loads & |
|  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC indication,

- One 3½ digit digital panel meter is provided to read output voltage,

,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  | b) One Coarse and one fine potentiometer to |
|  |  | Control the output voltage, |
|  |  | c) One Coarse and one fine potentiometer to |
|  |  | Control the output current, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required, |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR +/-5V/5A,+/-15V/5A,0-30V/0-5A

MULTI OUTPUT POWER  SUPPLY

| 1. | Model no | : UE-MPS-96. |
| --- | --- | --- |
| 2. | Mains input | : 220V, +10%, 50-6Hz, Single phase. |
| 3. | Type | : CV/CC. |
| 4. | Output | : a)+/-5V/5A, b)+/-15V/5A,c)0-30V/0-5A |
| 5. | Line Regulation | : + 0.1% max. Output Voltage for + 10% change |
|  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  | to full load or Vice-versa. |
| 7. | Ripple | : Less than 1mV R.M.S. |
| 8. | Protections | : a) Unit is protected by input fuse, |
|  |  | b) Unit is protected against input surges, |
|  |  | c) Output is protected against over loads & |
|  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC              indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  | b) One Coarse and one fine potentiometer to |
|  |  | Control the output voltage, |
|  |  | c) One Coarse and one fine potentiometer to |
|  |  | Control the output current, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |