SPECIFICATIONS FOR 0-16V/0-6A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-28. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-16V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-6A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

9. Indication(s)	:  a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided           to read output voltage,

- One 3½ digit digital panel meter is provided      to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 16V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 6A, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-20V/0-5A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-65. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-20V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-5A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |

c) Output is protected against over loads & Continuous short circuits.

| 9. | Indication(s) | : | a) One LED for input, |
| --- | --- | --- | --- |
|  |  |  | b) One LED each for CV and CC indication, |
|  |  |  | c) One 3½ digit digital panel meter is provided |
|  |  |  | to read output voltage, |
|  |  |  | d) One 3½ digit digital panel meter is provided |
|  |  |  | to read output current. |
| 10. | Controls | : | a) One ON/OFF switch to ON/OFF the Unit, |
|  |  |  | b) One Core and one fine potentiometer to |
|  |  |  | Control the output voltage from 0 to 20V, |
|  |  |  | c) One Core and one fine potentiometer to |
|  |  |  | Control the output current from 0 to 5A, |
|  | NOTE : | d) One potentiometer with locknut is |
|  |  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : | Bench top / 19” Rack Mounting as required by |
|  |  |  | you. |
| 12. | Cooling | : | Natural air cooling. |
| 13. | Operating Environment | : | 1) 0°C to +50°C |
| 14. | Terminals | : | Banana socket(s) at front panel & Piri Terminal |
|  |  |  | Strip with remote sensing at rear panel if |
|  |  |  | Required. |

SPECIFICATIONS FOR 0-24V/0-5A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-46. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-24V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-5A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |

c) Output is protected against over loads & Continuous short circuits.

9. Indication(s)	:  a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : | a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- | --- |
|  |  |  | b) One Core and one fine potentiometer to |
|  |  |  | Control the output voltage from 0 to 24V, |
|  |  |  | c) One Core and one fine potentiometer to |
|  |  |  | Control the output current from 0 to 5A, |
|  | NOTE : | d) One potentiometer with locknut is |
|  |  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : | Bench top / 19” Rack Mounting as required by |
|  |  |  | you. |
| 12. | Cooling | : | Natural air cooling. |
| 13. | Operating Environment | : | 1) 0°C to +50°C |
| 14. | Terminals | : | Banana socket(s) at front panel & Piri Terminal |
|  |  |  | Strip with remote sensing at rear panel if |
|  |  |  | Required. |

SPECIFICATIONS FOR 0-30V/0-2A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-29A. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-30V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-2A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |

c) Output is protected against over loads & Continuous short circuits.

9. Indication(s)	:  a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 30V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 2A, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Natural air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-30V/0-5A REGULATED DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-40. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-30V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-5A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |

c) Output is protected against over loads & Continuous short circuits.

9. Indication(s)	:  a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : | a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- | --- |
|  |  |  | b) One Core and one fine potentiometer to |
|  |  |  | Control the output voltage from 0 to 30V, |
|  |  |  | c) One Core and one fine potentiometer to |
|  |  |  | Control the output current from 0 to 5A, |
|  | NOTE : | d) One potentiometer with locknut is |
|  |  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : | Bench top / 19” Rack Mounting as required by |
|  |  |  | you. |
| 12. | Cooling | : | Natural air cooling. |
| 13. | Operating Environment | : | 1) 0°C to +50°C |
| 14. | Terminals | : | Banana socket(s) at front panel & Piri Terminal |
|  |  |  | Strip with remote sensing at rear panel if |
|  |  |  | Required. |

SPECIFICATIONS FOR 0-30V/0-10A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-3010. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-30V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-10A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

9. Indication(s)	:  a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

10. Controls	: a) One ON/OFF switch to ON/OFF the Unit,

- One Core and one fine potentiometer to Control the output voltage from 0 to 30V,

- One Core and one fine potentiometer to Control the output current from 0 to 10A,

NOTE  :      d) One potentiometer with locknut is

Provided for over voltage setting if required.

| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
| --- | --- | --- |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-32V/0-3A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-71. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-32V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-3A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |

c) Output is protected against over loads & Continuous short circuits.

9. Indication(s)	:  a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
| --- | --- | --- |
|  |  |  | b) One Core and one fine potentiometer to |
|  |  |  | Control the output voltage from 0 to 32V, |
|  |  |  | c) One Core and one fine potentiometer to |
|  |  |  | Control the output current from 0 to 3A, |
|  | NOTE : | d) One potentiometer with locknut is |
|  |  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  |  | you. |
| 12. | Cooling | : | Natural air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  |  | Strip with remote sensing at rear panel if |
|  |  |  | Required. |

SPECIFICATIONS FOR 0-32V/0-10A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-3010. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-32V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-10A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

9. Indication(s)	:   a) One LED for input,

- One LED each for ON CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

10. Controls                             :    a) One ON/OFF switch to ON/OFF the Unit,

- One Core and one fine potentiometer to Control the output voltage from 0 to 32V,

- One Core and one fine potentiometer to Control the output current from 0 to 10A,

NOTE :    d) One potentiometer with locknut is

Provided for over voltage setting if required.

| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
| --- | --- | --- |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-48V/0-10A VARIABLE DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-62B. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-48V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-10A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

9. Indication(s)	:    a) One LED for input,

- One LED each for CV and CC indication ,

- One 3½ digit digital panel meter is provided to read output voltage,

- One 3½ digit digital panel meter is provided to read output current.

10. Controls	:    a) One ON/OFF switch to ON/OFF the Unit,

- One Core and one fine potentiometer to Control the output voltage from 0 to 48V,

- One Core and one fine potentiometer to Control the output current from 0 to 10A,

- NOTE: One potentiometer with locknut is Provided for over voltage setting if required.

| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
| --- | --- | --- |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-3V/0-200A REGULATED DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-102. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-3V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-200A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

| 9. | Indication(s) | : a) One LED for input, |
| --- | --- | --- |
|  |  | b) One LED each for CV and CC indication |
|  |  | c) One 3½ digit digital panel meter is provided |
|  |  | to read output voltage, |
|  |  | d) One 3½ digit digital panel meter is provided |
|  |  | to read output current. |
| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 3V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 200A, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |

SPECIFICATIONS FOR 0-250V/0-5A REGULATED DC POWER SUPPLY

| 1. | Model no |  | : UE-VPS-47. |
| --- | --- | --- | --- |
| 2. | Mains input |  | : 230V, +10%, 50Hz, Single phase. |
| 3. | Type |  | : CV/CC. |
| 4. | Output | a) Voltage | : | 0-250V Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
|  |  | b) Current | : | 0-5A Variable continuously with coarse & fine |
|  |  |  |  | potentiometer mounted on front panel. |
| 5. | Line Regulation |  | : + 0.1% max. Output Voltage for + 10% change |
|  |  |  |  | in mains Input Voltage. |
| 6. | Load Regulation | : + 0.1% max. Output Voltage Change for No-load |
|  |  |  |  | to full load or Vice-versa. |
| 7. | Ripple |  | : Less than 2mV R.M.S. |
| 8. | Protections |  | : a) Unit is protected by input fuse, |
|  |  |  |  | b) Unit is protected against input surges, |
|  |  |  |  | c) Output is protected against over loads & |
|  |  |  |  | Continuous short circuits. |

| 9. | Indication(s) | : a) One LED for input, |
| --- | --- | --- |
|  |  | b) One LED each for CV and CC indication, |
|  |  | c) One 3½ digit digital panel meter is provided |
|  |  | to read output voltage, |
|  |  | d) One 3½ digit digital panel meter is provided |
|  |  | to read output current. |
| 10. | Controls | : a) One ON/OFF switch to ON/OFF the Unit, |
|  |  | b) One Core and one fine potentiometer to |
|  |  | Control the output voltage from 0 to 250V, |
|  |  | c) One Core and one fine potentiometer to |
|  |  | Control the output current from 0 to 5A, |
|  | NOTE | : d) One potentiometer with locknut is |
|  |  | Provided for over voltage setting if required. |
| 11. | Mechanical | : Bench top / 19” Rack Mounting as required by |
|  |  | you. |
| 12. | Cooling | : Forced air cooling. |
| 13. | Operating Environment | : 1) 0°C to +50°C |
| 14. | Terminals | : Banana socket(s) at front panel & Piri Terminal |
|  |  | Strip with remote sensing at rear panel if |
|  |  | Required. |